## Slide 1: The development of digital X-ray detector for osteodensitometry
Oleynikov Vladislav Petrovich
Scientific adviser – Porosev Vyacheslav Viktorovich
Ph.D. in Physics and Mathematics, Senior Scientist
Budker Institute of Nuclear Physics

## Slide 2: The main aim
osteodensitometr
detector

## Slide 3: At present, densitometers are not produced in Russia
Place of Origin: South Korea
Place of Origin: France

## Slide 4: Densitometer is a device that allows to determine bone mineral density

## Slide 5
There are three main ways of collecting information from the detector
1) integrating mode (signal is proportional to the number of detected photons)
2) counting mode (allows to distinguish each individual X-ray photon)
3) spectrometric mode (we not only separates each individual photon, but also register its energy)

## Slide 6: The detector
non-hygroscopic
bright
fast
high density and atomic number
high energy resolution
SiPM
Scintillator

## Slide 7: Two scintillators
YAP:Ce or LuYAG:Pr
CdTe is not technologically and requires special electronics
HPGe is too expensive for everyday use, because it requires cooling

## Slide 8: Selection of SiPM
KETEC
The main characteristic significantly affecting the energy resolution is quantum efficiency

## Slide 9: What is necessary energy resolution of the detector?
SiPM KETEC
YAP:Ce
17% energy resolution at the energy of 59.5 keV
20% (FWHM at an energy of 40 keV (estimation)

## Slide 10: Self-consistent model
the response of the detector
the incident X-ray spectrum
the number of particles in it
the error of determining bone density

## Slide 11: The case of two monoenergetic sources

## Slide 12: At present
a more precise and complex model

## Slide 13: Conslusions
one produced detector based on the combination of SiPM - scintillator allowing to achieve 17% energy resolution at the energy of 59.5 keV with high counting rate
The model of the two monoenergetic sources allowing in the first approximation to estimate the error of determining bone density was considered

## Slide 14: Thank you for your attention!